DAC and ADC

---
All about data
Embedded systems
  - Need to process data
    - Sample status of the environment
    - But, raw data is analogous
  - Need to display data
    - Control devices
    - But, control signal is analogous
Chips
  - Amplifier/Comparator
  - DAC
  - ADC

---
Circuit model
- Amplifier model
- Comparator model
V_{o} = - {{R2} over {R1}} V_{i}
V_{o} = - {{R_{1}} over {R_{2}}} V_{1} + {(R_{1}+R_{2}) R_{4}} over {R_{2} (R_{3}+R_{4})} V_{2}

---
Amplifier
INA2128
  - How to determine gain
  - What is the power supply
  - What is the output range (for sample)
  - What is the input range (for control)
  - How does it respond to input signals with various frequencies (for control)
  - Example circuit: acoustic, temperature, ...

---
Amplifier/Comparator
- For comparator,
  - If all resistors are the same,
- Negation and addition circuits
  - Negation?
  - Addition?
V_{1} - V_{2} = -V_{0}

---
DAC
- Digital-to-Analog Converter
- Circuit model
  - Reference voltage
  - Amplifier
  - Analog adder
  - Analog switch

---
DAC
- Principle
  - Input : 0110
  - Output = 0*8 + 1*4 + 1*2 + 0*1
  - Reference voltage ?
  - Amplifier ?
  - Anolog adder ?
  - Analog switch ?

---
DAC
- Performance
  - Resolution
    - 2number_of_bits
  - Total harmonic distortion
    - Rectangle output vs. smooth output
  - Noise
  - Dynamic output range

---
DAC
- Example, AD7304
  - Electrical features
    - Resolution : 8 bits
    - Input resistance : 28KOhm
    - Reference : <5V, from outside
    - Output voltage range : <5V
    - Output current drive : 3mA
    - Logic voltage : 0.8V as low, 2.4V as high
    - Timing : around 50 ns, so safe time is 100ns
    - Operating Temperature Range

---
DAC (AD7304)
- Example
  - Input
    - Serial :
      - SPI-compatible serial data interface
      - 12-bit data-word format, table 5
      - MSB bits are loaded first
      - Timing
      - How fast is the data rate after all (Bps, not bps)?
    - No parallel

---
DAC (AD7304)
Example of control

---
DAC (AD7304)
- Control by embedded software
  - 1. Configure four IO pins to output
    - SDI, CLK, CS, LDAC
  - 2. Prepare 12-bit data (SDI)
  - 3. Output 1 to the LDAC pin
  - 4. Output 0 to the CS pin
  - 5. Repeat 12 times
    - 5.1. Output the MSB of SDI to the SDI pin
    - 5.2. Output a clock (CLK) to the CLK pin
      - A low and a high
    - 5.3. Left shift SDI
  - 6. Output 1 to the CS pin
  - 7. Output 0 to the LDAC pin

---
DAC (AD7305)
- Control
  - How many pins
  - Control logic

---
ADC
- Analog-to-Digital Converter
- Operation theory
  - Sampling (too low vs too fast)
  - Nyquist theory (proper sampling rate)
    - The sampling rate should at least double the highest frequency of the signal.
  - Sound : 10 Hz to 10KHz
    - Sampling rate? Data rate?
  - Ultrasound for diagnose : 200KHz to 2MHz

---
ADC
- Performance
  - Resolution
  - Maximum sampling frequency
  - Noise
  - Dynamic input range

---
ADC
Type
  - Linear ADC
    - Output = c * Input
    - Distortion = σ2/2, where σ is the interval of resolution
  - Non-linear ADC
    - Ouput = c * log2(input)
    - Distortion = ?

---
ADC
- Implementation
  - Direct conversion ADC
    - A voltage ladder producing (2^n-1) voltages
    - (2^n-1) comparators
    - An encoder
      - How?
    - Extremely fast, but hard to have a very high resolution
      - 8 bits, OK; 12 bits ?; 16 bits NO
  - Example, a 2-bit ADC

---
ADC
- Implementation
  - Successive-approximation ADC
    - A comparator
    - A DAC
    - A shift register
    - Procedure
      - MSB 1, all others 0
      - Compare Vin>VDAC?
      - Yes, 1->MSB; No, 0->MSB
      - Next bit, ...
    - How fast?

---
ADC (AD7476)
- Example
  - Electricity features
    - Throughput : 1MSPS
    - fSCLK : 10M or 20M
    - 12 bits
  - Output
    - Serial
    - Timing ?
    - Interface to CPUs ?

---
ADC (AD7476)
- Control
  - The conversion is initiated on the falling edge of CS as de-scribed in the Serial Interface section.
  - To ensure the part remains fully powered up at all times, CS must remain low until at least 10 SCLK falling edges have elapsed after the falling edge of CS.
  - 16 serial clock cycles are required to complete the conversion and access the complete conversion result.

---
ADC (AD7476)
- Control logic
  - Output low to CS
  - Output 16 clocks
    to SCLK
  - Output high to CS
  - Read DR

---
Design with ADC (AD7476)
- Sample a signal of 20KHz
  - Can AD7476 work on this?
    - Sample rate?
    - Resolution?
  - Can the CPU ATMega128 (8MHz) work on this?
    - Time for each reading?
    - What is the duty cycle (percentage of working time)?
  - What is the minimum requirement on ADC and CPU for this application?
    - Speed
    - Power

---
ADC (in chip)
- Example, ATmega128, in chip
  - Electrical features
    - 15KSPS
    - 10 bits
    - 8 input channels (multiplexed single end)
    - Internal adjustable gains
  - Output
    - Parallel
    - 16-bit output register
    - Two configuration registers

---
ADC
Circuit
model

---
ADC (in chip)
Control

---
Now,
We have binary data!