CPU II
Design
Chapter 4

---
CPU Model
Processor pins
  - Power supply
  - Ground
  - Clock
  - Address pins
  - Data pins
  - IO pins
  - Read pin (to memory)
  - Write pin (to memory)
  - Interrupt pins

---
CPU Model

---
Execution Cycle
- Determine instruction
- Fetch instruction
- Decode instruction
- Fetch operands
- Execute
- Store result
- ...

---
Execution Cycle

---
CPU Core Components
ALU
  - Computation unit
Register
  - Fast data storage
Control unit
  - Management unit
Internal bus
  - Connect the three components

---
CPU Core Components

---
Internal Bus
- Control signals + tri-state gates
- Types
  - Data bus
    - Data mem, registers, IOs
  - Address bus
    - Program counter (to code mem)
    - Registers (to data mem)
  - Control bus
    - Instruction decoder

---
ALU
Arithmetic instructions
  - Integer and floating arithmetic computation
  - Signed and unsigned addition and subtraction
  - Multiplication? (*)
  - Division? (/ %)
  - Logarithm, exponentiation, ??
Logic instructions
  - AND, OR, XOR
  - NOT : 1's and 2's complements

---
ALU
- Branch instructions
  - Conditional branch
  - Jump : direct, indirect, relative, absolute
  - Call, return : direct, indirect, relative, absolute
- Data transfer instructions
  - Mem to and from reg
  - Reg to reg, mem to mem
  - Mem and reg to and from IO
  - Code mem to and from data mem

---
ALU
- Bit and bit testing instructions
  - Set, clear
  - Swap, shift
  - Test
- MCU and MMU control instructions
  - NOP
  - Sleep (pause)
  - Soft interrupt
  - Memory control and map

---
Registers
- Store operands and results
- Made by flip-flop or SRAM
- Storage register vs. shift register
- Special registers
  - Status register
    - State of a processor
  - Timer
  - Program counter

---
Control Unit
Fetch instruction
  - Sequential
  - Branch
Fetch operands
  - Pipeline
Control execution
  - Select functional unit
  - Signal functional unit

---
CPU Clock
- External clock
- Internal clocks
  - Generation
    - How? (RC delay)
  - Divide
    - How? (Counter)

---
On-chip Memory
Non-volatile memory
  - Data in memory will not disappear
  - Read-only memory (ROM) : Figure 4-39
  - Programmable link/fuse : Figure 4-40
  - Types
    - MROM
    - PROM
    - EPROM
    - EEPROM
    - Flash

---
Volatile Memory
- Random-access memory (RAM)‏
- Types
  - SRAM : flip-flop
  - DRAM : capacitor
    - Discharge when read or overtime
    - Need recharge / refresh
    - Refresh is controlled by memory controller

---
Cache
Level-1 cache
  - Inside CPU
    - Cache vs. on-chip main memory
  - Snapshot of a part of main memory
  - Directly interact with the CPU
  - Most code only access code and data within a range
  - Cache hit vs. cache miss

---
Cache
Data transfer between cache and main memory
  - Consistency
  - Read criteria : high hit rate and low miss rate
  - Write strategies
    - Write through
    - Write back
  - CPU and memory architecture
    - CPU↔cache↔MMU↔memory↔DMA↔HD

---
On-chip Memory Management
Functionalities
  - Control multiple physical memories
  - Translate logical address to physical address
  - Handle memory security
  - Control cache
  - Handle bus arbitration between CPU and memory
Memory organization
  - Code and data memory
  - Memory mapping

---
Example: Memory and IO Mapping
- 256 IOs
- 1 64KB ROM (flash)
- 3 64KB RAMs
- Von-Nueman architecture
- Mapping (20-bit address space)
  - 0x00 - 0xFF IOs (share space with ROM)
  - 0x100 - 0xFFFF code in ROM
  - 0x10000 - 0x3FFFF data in RAMs
  - A selection signal on 0x000XX

---
Processor I/O
Most concepts are the same as board I/O
  - because the boundary of a board and a processor in an embedded system is not as clear as in a regular computer.
I/O pin
  - Unidirectional (in or out)‏
  - Bidirectional (in and out)‏
  - Programmable

---
IO Pin Example

---
IO Pin Example
- LEDs
  - Connected to pin set A: 0, 1, 2
  - Two registers control pin set A
    - DDRA ($1A ($3A)) : direction control
      - 0 : input
      - 1 : output
    - PORTA ($1B ($3B)) : data output
    - PINA ($19 ($39)) : data input

---
Embedded I/O Components
Serial I/O
  - USART ( example in sensor)
    - Universal Synchronous Asynchronous Receiver Transmitter
  - SPI
    - Serial Peripheral Interface
  - JTAG
    - Joint Test Action Group, IEEE 1149.1
    - Diagnose software and hardware of embedded system

---
JTAG
- Debug support is for many software developers the main reason to be interested in JTAG.
- Debugging architectures built up using JTAG, such as ARM CoreSight, Nexus, ...
- Processors can normally be halted, single stepped, or let run freely.
- Code breakpoints are supported, both for code in RAM and in ROM/flash.
- Data breakpoints are often available, as is bulk data download to RAM.

---
JTAG
- JTAG pins
  - TDI (Test Data In) : input JTAG instructions
  - TDO (Test Data Out) : obtain scanned data
  - TCK (Test Clock) : clock, SPI
  - TMS (Test Mode Select) : state control
  - TRST (Test Reset) optional

---
JTAG
- Examples of JTAG instructions
  - EXTEST : for external testing, such as using pins to probe board-level behaviors
  - INTEST : for internal testing, such as using pins to probe on-chip behaviors
  - PRELOAD : loading pin output values before EXTEST
  - SAMPLE : reading pin values into the boundary scan register
  - HIGHZ : deactivates the outputs of all pins
  - RUNBIST : places the chip in a self-test mode
  - SCAN_N : configures a scan path select register (SCREG) affecting the signals to which other boundary scan operations apply
  - USERCODE : returns a user-defined code, for example to identify which FPGA image is active
  - HALT, RESTART : halts or restarts the CPU.

---
JTAG Example
- Boundary-scan Capabilities
- Debugger Access to:
  - All Internal Peripheral Units
  - Internal and External RAM
  - The Internal Register File
  - Program Counter
  - EEPROM and Flash Memories
- Extensive On-chip Debug Support for Break
  - AVR Break Instruction
  - Break on Change of Program Memory Flow
  - Single Step Break
  - 4 : Program Memory Breakpoints + Data Memory Breakpoints
- Programming of Flash, EEPROM, Fuses, and Lock Bits
- On-chip Debugging Supported by AVR Studio

---
JTAG Example

---
Interrupts
Hardware interrupt
  - Internal
    - Timer, MMU, ADC, operation error, debugging
  - External
    - Hard drive, reset,
Software interrupt
  - INT instruction
    - Trigger a special routine to change context or mode
Interrupt vector

---
Interrupt Service
Service routine (pseudo-code)
  - When an interrupt is triggered, normally the interrupt flag is cleared to disable other interrupts.
  - Save context
  - Enable other interrupts (optional, set the interrupt flag)‏
  - Execute the interrupt routine
  - Disable other interrupts (clear the interrupt flag)‏
  - Restore context
  - Return (normally the interrupt flag is set by the return)‏
Example : case8.interrupt

---
External Interrupt
Trigger hardware
  - Interrupt pins (IRQs)‏
  - Interrupt controller
Trigger mechanism
  - Level-trigger
  - Edge-trigger
Interrupt controller
  - Slave processor + I/O device

---
Processor Performance
Computational performance
  - Throughput : instructions per second (MIPS)‏
  - Reliability : mean time between two failures
  - Recoverability : mean time from fail to normal
  - Availability : mean time from normal to fail
Power performance
  - Duty percentage : mean percentage of execution
  - Idle-mode power consumption